## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2018
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 10
Preserve Environment via Stack

## Slide 2: Stack
A Last-In-First-Out data structure
Only allow to access the most recently added item
  Also called the top of the stack
Key operations:
  push (add item to stack)
  pop (remove top item from stack)

## Slide 3: Tower of Hanoi
Only one disk may be moved at a time.
Each move consists of taking the upper disk from one of the rods and sliding it onto another rod, on top of the other disks that may already be present on that rod.
No disk may be placed on top of a smaller disk.

## Slide 4: Tower of Hanoi
http://en.wikipedia.org/wiki/File:Tower_of_Hanoi_4.gif
STACK: Last In First Out
Stack 1
Stack 2
Stack 3

## Slide 5: Stack Growth Convention: Ascending vs Descending
  Descending stack: Stack grows towards low memory address
  Ascending stack: Stack grows towards high memory address

## Slide 6: Stack Growth Convention: Full vs Empty
  Full stack: SP points to the last item pushed onto the stack
  Empty stack: SP points to the next free space on the stack

## Slide 7: Cortex-M Stack
stack pointer (SP) = R13
Cortex-M uses full descending stack
stack pointer
  decremented on PUSH
  incremented on POP
  SP starts at 0x20000200 for STM32-Discovery

## Slide 8: Full Descending Stack

## Slide 9: Stack Implementation
Stock Name | Push |  | Pop | 
 | Equivalent | Alternative | Equivalent | Alternative
Full Descending(FD) | STMFD SP!,list | STMDB SP!,list | LDMFD SP!,list | LDMIA SP!,list
Empty Descending(ED) | STMED SP!,list | STMDA SP!,list | LDMED SP!,list | LDMIB SP!,list
Full Ascending(FA) | STMFA SP!,list | STMIB SP!,list | LDMFA SP!,list | LDMDA SP!,list
Empty Ascending(EA) | STMEA SP!,list | STMIA SP!,list | LDMEA SP!,list | LDMDB SP!,list

## Slide 10: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.

## Slide 11: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Push multiple registers
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.

## Slide 12: Full Descending Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}

## Slide 13: Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}

## Slide 14: Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}

## Slide 15: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx

## Slide 16: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
xxxxxxxx

## Slide 17: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 18: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 19: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x11111111
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 20: Quiz
Are the values of R1 and R2 swapped?
  PUSH {R1, R2}
  POP {R2, R1}
Answer: No.
But you can:
  PUSH {R1, R2}
  POP {R2}
  POP {R1}
or
  PUSH {R1}
  PUSH {R2}
  POP {R1, R2}

## Slide 21: Subroutine
A subroutines, also called a function or a procedure,
  single-entry, single-exit
  Return to caller after it exits
When a subroutine is called, the Link Register (LR) holds the memory address of the next instruction to be executed after the subroutine exits.

## Slide 22: Link Register
Link Register (LR) holds the return address of the current subroutine call.

## Slide 23: Call a Subroutine
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101, not 11 | foo PROC ... MOV r4, #10 ; foo changes r4 ... BX LR ENDP

## Slide 24: Calling a Subroutine
BL label
Step 1: LR = PC + 4
Step 2: PC = label
Notes:
  label is name of subroutine
  Compiler translates label to memory address
  After call, LR holds return address (the instruction following the call)
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 25: Exiting a Subroutine
BX LR
PC = LR
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 26: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | YES | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 27: Link Register
Scratch registers, not saved by subroutine. Hold arguments/result
Link Register
Callee must save them.
Caller expects these values are retained .

## Slide 28: Preserve Runtime Environment via Stack
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101, not 11 | foo PROC PUSH {r4} ; preserve r4 ... MOV r4, #10 ; foo changes r4 ... POP {r4} ; Recover r4 BX LR ENDP

## Slide 29: Stacks and Subroutines

## Slide 30: Subroutine Calling Another Subroutine
MAIN
MOV R0,#2
BL QUAD
ENDL ...
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
SQ MUL R0,R0
BX LR
Function MAIN
Function QUAD
Function SQ

## Slide 31: Subroutine Calling Another Subroutine
MAIN PROC
MOV R0,#2
BL QUAD
ENDL ...
ENDP
QUAD PROC
PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDP
SQ PROC
MUL R0,R0
BX LR
ENDP
Function MAIN
Function QUAD
Function SQ

## Slide 32: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
R0
PC
0x08000138
LR
SP
0x20000200
SQ
QUAD

## Slide 33: Example: R0 = R04
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800013C
LR
SP
0x20000200
SQ
QUAD
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 34: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800014C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Preserve
Link Register (LR)
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 35: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x08000140
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000150
LR
SP
0x200001FC
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 36: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 37: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 38: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000154
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 39: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 40: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 41: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000158
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 42: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x0800015C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Recover
Link Register (LR)
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
0x08000140

## Slide 43: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000140
LR
SP
0x20000200
0x08000140
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 44: Initializing the stack pointer (SP)
Before using the stack, software has to define stack space and initialize the stack pointer (SP).
The assembly file startup.s defines stack space and initialize SP.