## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2018
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Stack and Recursive Functions

## Slide 2: Recursive Functions
A recursive function is one that solves its task by calling itself on smaller pieces of data.
An effective tactic is to
  divide a problem into sub-problems of the same type as the original,
  solve those sub-problems, and
  combine the results

## Slide 3: Defining Factorial(n)
1 × 2 × 3 × … × n
factorial(0)
= 1
factorial(1)
= 1
= 1 × factorial(0)
factorial(2)
= 2×1
= 2 × factorial(1)
factorial(3)
= 3×2×1
= 3 × factorial(2)
factorial(4)
= 4×3×2×1
= 4 × factorial(3)
factorial(n)
= n×(n-1)×…×1
= n × factorial(n-1)
Product of the first n numbers

## Slide 4: Classic Example: Factorial
Factorial is the classic example:
  6! = 6  5!
  6! = 6  5 x 4!
  …
  6! = 6  5  4  3  2  1
The factorial function can be easily written as a recursive function:
int Factorial(int n) {
if (n < 2)
return 1; /* base case */
return (n * Factorial(n – 1));
}

## Slide 5: Classic Example: Fibonacci Numbers
f(n) = f(n-1) + f(n-2)
f(0) = 1
f(1) = 1
1, 1, 2, 3, 5, 8, 13, 21, 34, 55, 89, 144, 233, 377, 610, 987, …
int Fibonacci(int n) {
if (n <= 1)
return 1; /* base case */
return (Fibonacci(n-1) + Fibonacci(n-2));
}

## Slide 6: Analysis of fib(5)
int fib(int n)
if(n == 0 || n == 1)
return n;
else
return fib(n-1) + fib(n-2);
fib(5)
fib(4)
fib(3)
fib(3)
fib(2)
fib(1)
fib(0)
fib(2)
fib(1)
fib(0)
fib(1)
fib(2)
fib(1)
fib(0)
fib(1)
1
1
1
1
1
0
0
0
1
1
2
1
3
2
5

## Slide 7: Example of Recursive Function: Testing Palindrome
bool isPalindrome(char* s, int len) {
if(len < 2)
return TRUE;
else
return s[0] == s[len-1] && isPalindrome(&s[1], len-2);
}

## Slide 8: Recursion vs Iteration
Any problem that can be solved recursively can also be solved iteratively (using loop).
Recursive functions vs Iterative functions
Cons:
  Recursive functions are slow
  Recursive function take more memory
Pros
  Recursive functions resembles the problem more naturally
  Recursive function are easier to program, and debug.

## Slide 9: Recursive Factorial in C
factorial(5)
5 * factorial(4)
4 * factorial(3)
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6
return 24
return 120
int factorial(int n);
int main(void){
factorial(5);
return 0;
}
int factorial(int n) {
int f;
if(n==1)
return 1;
else
f = n * factorial(n-1);
return f;
}

## Slide 10: Recursive Functions
push LR (& working registers) onto stack before nested call
pop LR (& working registers) off stack after nested return

## Slide 11: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 12: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000130
0xFFFFFFFF
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 13: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000136
0x08000134
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 14: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000138
0x08000134
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Order in which registers are specified is not important: the lowest register is always stored at the lowest address

## Slide 15: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000144
0x08000134
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 16: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000136
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 17: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000138
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 18: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000144
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 19: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000136
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 20: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000138
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
1
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 21: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x0800013E
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
1
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 22: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 23: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 24: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000140
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Order in which registers are specified is not important.

## Slide 25: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 26: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 27: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 28: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000134
0x08000148
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 29: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0x08000134
0x08000134
0x08000148
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C